## Slide 1
NORTH-WEST CORNER METHOD
The North West corner rule is a technique for calculating an initial feasible solution for a transportation problem. In this method, we must select basic variables from the upper left cell, i.e., the North-west corner cell
North West Corner Rule Steps
Step 1: Select the upper-left cell, i.e., the north-west corner cell of the transportation matrix and assign the minimum value of supply or demand, i.e., min(supply, demand).
Step 2: Subtract the above minimum value from Oi and Di of the corresponding row and column. Here, we may get three possibilities, as given below.
If the supply is equal to 0, strike that row and move down to the next cell.
If the demand equals 0, strike that column and move right to the next cell.
If supply and demand are 0, then strike both row and column and move diagonally to the next cell.
Step 3: Repeat these steps until all the supply and demand values are 0
*****Important: A transportation problem is called a balanced transportation problem if summation of supply = summation of demand. Before starting any Transportation problem one should check that the supply is equal to demand.

## Slide 2
Transportation Problem
Unbalanced Transportation Problem
Demand>Supply
Add a Dummy Row with cost zero and the supply becomes (DEMAND-SUPPLY)
Balanced Transportation Problem
Demand=Supply
Demand<Supply
Add a Dummy Column with cost zero and the Demand becomes (SUPPLY-DEMAND)
TYPES OF TRANSPORTATION PROBLEMS

## Slide 3
 | D1 | D2 | D3 | D4 | SUPPLY
O1 | 3 | 1 | 7 | 4 | 300
O2 | 2 | 6 | 5 | 9 | 400
O3 | 8 | 3 | 3 | 2 | 500
DEMAND | 250 | 350 | 400 | 200 | 
Example-1 (Balanced Transportation Problem)

## Slide 4
 | D1 | D2 | D3 | D4 | SUPPLY
O1 | 3 [250] | 1 | 7 | 4 | 300 50
O2 | 2 | 6 | 5 | 9 | 400
O3 | 8 | 3 | 3 | 2 | 500
DEMAND | 250 (0) | 350 | 400 | 200 | 
 | D2 | D3 | D4 | SUPPLY
O1 | 1 [50] | 7 | 4 | 50 (0)
O2 | 6 | 5 | 9 | 400
O3 | 3 | 3 | 2 | 500
DEMAND | 350 300 | 400 | 200 | 
STEP-1
STEP-2

## Slide 5
 | D2 | D3 | D4 | SUPPLY
O2 | 6 [300] | 5 | 9 | 400 (100)
O3 | 3 | 3 | 2 | 500
DEMAND | 350 300 (0) | 400 | 200 | 
 | D3 | D4 | SUPPLY
O2 | 5 [100] | 9 | 100 (0)
O3 | 3 | 2 | 500
DEMAND | 400 (300) | 200 | 
STEP-3
STEP-4

## Slide 6
 | D3 | D4 | SUPPLY
O3 | 3 [300] | 2 | 500 (200)
DEMAND | 300 | 200 | 
 | D4 | SUPPLY
O3 | 2 [200] | 200 (0)
DEMAND | 200 (0) | 
STEP-5
STEP-6

## Slide 7
 | D1 | D2 | D3 | D4 | SUPPLY
O1 | 3[250] | 1[50] | 7 | 4 | 300
O2 | 2 | 6[300] | 5[100] | 9 | 400
O3 | 8 | 3 | 3[300] | 2[200] | 500
DEMAND | 250 | 350 | 400 | 200 | 
Now just multiply the allocated value with the respective cell value (i.e. the cost) and add all of them to get the basic solution i.e. (250 * 3) + (50 * 1) + (300 * 6) + (100 * 5) + (300 * 3) + (200 * 2) = 4400

## Slide 8
Example-1 (Unbalanced Transportation Problem)
 | D1 | D2 | D3 | SUPPLY
O1 | 4 | 8 | 8 | 76
O2 | 16 | 24 | 16 | 82
O3 | 8 | 16 | 24 | 77
DEMAND | 72 | 102 | 41 | 
Supply:-76+82+77=235
Demand:-72+102+41=215
Supply is not equal to Demand

## Slide 9
 | D1 | D2 | D3 | D(dummy) | SUPPLY
O1 | 4 | 8 | 8 | 0 | 76
O2 | 16 | 24 | 16 | 0 | 82
O3 | 8 | 16 | 24 | 0 | 77
DEMAND | 72 | 102 | 41 | 235-215=20 | 
 | D1 | D2 | D3 | D(dummy) | SUPPLY
O1 | 4 | 8 | 8 | 0 | 76
O2 | 16 | 24 | 16 | 0 | 82
O3 | 8 | 16 | 24 | 0 | 77
DEMAND | 72 | 102 | 41 | 20 | 
STEP-1
STEP-2

## Slide 10
 | D1 | D2 | D3 | D(dummy) | SUPPLY
O1 | 4 [72] | 8 | 8 | 0 | 76 (4)
O2 | 16 | 24 | 16 | 0 | 82
O3 | 8 | 16 | 24 | 0 | 77
DEMAND | 72 (0) | 102 | 41 | 20 | 
 | D2 | D3 | D(dummy) | SUPPLY
O1 | 8 [72] | 8 | 0 | 4 (0)
O2 | 24 | 16 | 0 | 82
O3 | 16 | 24 | 0 | 77
DEMAND | 102(98) | 41 | 20 | 
STEP-3
STEP-4

## Slide 11
 | D2 | D3 | D(dummy) | SUPPLY
O2 | 24 [82] | 16 | 0 | 82 (0)
O3 | 16 | 24 | 0 | 77
DEMAND | 98 [16] | 41 | 20 | 
 | D2 | D3 | D(dummy) | SUPPLY
O3 | 16 [16] | 24 | 0 | 77 [61]
DEMAND | 16 (0) | 41 | 20 | 
STEP-5
STEP-6

## Slide 12
 | D3 | D(dummy) | SUPPLY
O3 | 24 [41] | 0 | 61 (20)
DEMAND | 41 (0) | 20 | 
 | D(dummy) | SUPPLY
O3 | 0 [20] | 20 (0)
DEMAND | 20 (0) | 
STEP-8
STEP-7

## Slide 13
 | D1 | D2 | D3 | D(dummy) | SUPPLY
O1 | 4[72] | 8[4] | 8 | 0 | 76
O2 | 16 | 24[82] | 16 | 0 | 82
O3 | 8 | 16[16] | 24[41] | 0[20] | 77
DEMAND | 72 | 102 | 41 | 20 | 
Minimum Cost=(4*72)+(8*4)+(24*82)+(16*16)+(24*41)+(0*20)=3528